## Slide 1
LPC2129
ARM7TDMI-S
60 MHz
CAN Bus
100 kbps
0x212–0x217
ARM-Based Real-Time
Digital Automotive
Instrument Cluster
CAN Protocol Integration • LPC2129 • Bare-Metal C
ADC Sensors
16×2 LCD
CAN 2.0B
VECTOR INDIA PVT LTD,
BANGALORE
Precented By-
GOPI SHANKAR V - V25BE5G12
KABULLA P - V25BE5P9
UDAY KIRAN C - V25BE5C2
VISHAL K - V25BE5V7

## Slide 2
System Overview
End-to-end architecture: sensors → CAN bus → display
NODE A
Sensor & Input Node
Speed Sensor
(ADC ch2 P0.29)
Temp Sensor
(ADC ch1 P0.28)
Buttons EINT0/1/2
CAN 2.0B
BUS
100 kbps
IDs: 0x212–0x216
TX
NODE B
Display & Output Node
16×2 LCD Display
(4-bit, Port 1)
LED Indicators
(P0.17/18/19)
CAN RX ISR
+ Acceptance Filter
RX

## Slide 3
Node A — Sensor & Transmitter
LPC2129 reads sensors and switch states, then transmits 6 CAN message types
Speed Pot
ADC ch2
P0.29
LM35 Temp
ADC ch1
P0.28
Left Indicator
EINT0
P0.16
Right Indicator
EINT1
P0.14
Head Light
EINT2
P0.15
LPC2129
Timer1 ISR
(1 sec tick)
EINT0/1/2 ISR
ADC Driver
CAN2 TX
0x215
Speed
0x216
Temp
0x212
Left Indi.
0x214
Right Indi.
0x213
Head Light
CAN2 TX → Node B

## Slide 4
Node B — Display & Output
CAN RX interrupt → decode message → update LCD / LEDs / Buzzer
LPC2129
CAN2 RX ISR
Acceptance Filter
0x212–0x217
LCD 4-bit Driver
+ CGRAM chars
GPIO LED Control
0x212 — Left Indi.
0x213 — Head Light
0x214 — Right Indi.
0x215 — Speed ADC
0x216 — Engine Temp
16×2 LCD
(Port 1, 4-bit mode)
Left Indicator LED
P0.17
Head Light LED
P0.18
Right Indicator LED
P0.19

## Slide 5
CAN Protocol — Frame Structure & Message Table
SOF
ID
(11-bit)
RTR
DLC
(4-bit)
DATA
(0–8 bytes)
CRC
(15-bit)
ACK
EOF
Standard CAN 2.0A / 2.0B Frame • 100 kbps • LPC2129 CAN2 Controller
CAN ID
Source
byteA Value
Meaning
Recipient
0x212
Node A
0x02 / 0x03
Left Indicator ON / OFF
Node B
0x213
Node A
0x04 / 0x05
Head Light ON / OFF
Node B
0x214
Node A
0x06 / 0x07
Right Indicator ON / OFF
Node B
0x215
Node A
0–1023 (raw)
Speed ADC value
Node B
0x216
Node A
0–1023 (raw)
Engine Temperature ADC
Node B

## Slide 6
16×2 LCD Display Layout
←
☀
→
1
2
3
k
m
/
h
4
5
.
6
°
Col: 0 1 2 3 4 5 6 7 8 9 10 11 12 13 14 15
← Left Indicator
(CGRAM slot 0)
☀ Head Light
(CGRAM slot 1)
→ Right Indicator
(CGRAM slot 2)
Speed
0–200 km/h
Engine Temp
°C (LM35)

## Slide 7
ADC & Sensor Interface
10-bit on-chip ADC • Software-triggered single conversion • 60 MHz PCLK
Speed Channel (ADC ch2)
Potentiometer
(0–3.3V)
P0.29
AD0.2 pin
ADCR SEL
bit-2 set
10-bit Conv
~25 cycles
ADDR[15:6]
Result reg
0x215
CAN TX
Temperature Channel (ADC ch1)
LM35 Sensor
10mV/°C
P0.28
AD0.1 pin
ADCR SEL
bit-1 set
10-bit Conv
~25 cycles
ADDR[15:6]
Result reg
0x216
CAN TX
Key ADC Registers
PINSEL1
[25:24]=01 & [27:26]=01
Route P0.28,29 to ADC
ADCR
[21]=1 (PDN), [26:24]=001
Power-up, start conversion
ADDR
[15:6]=result, [31]=DONE
Read 10-bit result

## Slide 8
Interrupt Architecture — VIC & Timer
LPC2129 Vectored Interrupt Controller routes 4 sources into Node A firmware
VIC
Vectored Interrupt
Controller
Slot 0 Src 15
EINT1_Handler
Slot 1 Src 14
EINT0_Handler
Slot 2 Src 5
TIMER1_Handler
Slot 3 Src 16
EINT2_Handler
P0.14 EINT1
Right
Indicator Btn
P0.16 EINT0
Left
Indicator Btn
Timer 1 MR0
1-sec ADC
P0.15 EINT2
Head
Light Btn
flag2 = 1
CAN TX 0x214
Right indicator
flag1 = 1
CAN TX 0x212
Left indicator
flag = 1
ADC read ch1,ch2
flag3 = 1
CAN TX 0x213
Head light
Timer1 Formula: T1PR = PCLK − 1 = 59,999,999 | T1MR0 = 1 | T1MCR = 3 (Interrupt + Reset) → 1 second period @ 60 MHz PCLK

## Slide 9
Project
Summary
⚡
ARM7TDMI-S @ 60MHz
LPC2129 bare-metal C
📡
CAN 2.0B @ 100 kbps
6 message IDs, acceptance filter
🖥
16×2 LCD 4-bit mode
CGRAM arrows & sun symbols
🔄
4 Interrupt sources
VIC, EINT0/1/2, Timer1
🌡
ADC sensors
Speed ch2 + Temperature ch1
Deliverable Files
Node A (Sensor / TX)
header.h
delay.c
ADC.c
CAN-driver.c
Amain.c
eint0.c / eint1.c / eint2.c
timer_interrupt.c
Node B (Display / RX)
header.h
delay.c
lcd4-bit-driver.c
CAN-driver.c
Bmain.c
ARM Bare-Metal • Real-Time • CAN Protocol • Automotive Cluster